Phaenovum RaspiCar: Interface biard command list

SLW - November 2025

Interface description

The interface board is connected to the Raspberry Pi via USB port 0, typically /dev/ttyUSB0. Communication is established by a serial interface at (baudrate 115200, no parity bit). The communication is bidirectional. The Raspberry Pi sends a command and receives a response. All commands must be terminated by a “carriage return” symbol (code 13, \n). The script on the Raspberry Pi can use the response to check whether the command was processed as expected.

Command List

Motor commands:
- MD <dir_a>, <dir_b>
  Sets the direction for both motors. The value 1 stands for forward, and the value 0 for backwards.
  Example: MD0,1
- ME <enable_a>, <enable_b>
  Enables or disables the motors. The value 1 stands for enabled, and the value 0 for disabled.
  Example: ME1,0
- MP <power_a>, <power_b>
  Activates the motor power. The value 1 stands for power on, and the value 0 for power off. This command enables the motors implicitly.
  Example: MP1,1
- MR <speed_a>, <speed_b>
  Sets the motor speed. The valid range is 0 to 1250. The motor must be enabled and powered on in order to start rotation.
  Example: MR200,500

Display commands:
- DC
  Clears the display.
  Example: DC
- DT<message>
  Prints a title line. The maximum length is 20 characters.
  Example: DTVersion2.1
- DM<message>
  Prints a message to the display. The content of the display will be scrolled up.
  Example: DMRaspPi connected

Battery commands:
- BV
  Get battery voltage. The system will respond with the current voltage of the power supply.
- BS
  Get battery status. The system will respond with one of the following codes::
  'OK'	STATUS_OK
'BL'	STATUS_BAT_LOW
'BS'	STATUS_BAT_SHUTDOWN
'BE'	STATUS_BAT_EXTERNAL
'SR'	STATUS_SHUTDOWN_REQUESTED
'SX'	STATUS_SHUTDOWN_ACTIVE
BX
Request a system shutdown.